## Slide 1
COMMUNICATIONS DEPARTMENT: Ground station
Boyan Naydenov, Josep Puig, Josep Maria Serra, Sergi Tarroc and Eva María Urbano

## Slide 2: What are we going to talk about?
Work done:
  Critical failure
  Ground station
    Location
    Cost

## Slide 3: Critical failure
Project charter deffinition
New deffinition
A major failure can be defined as the loss of a client’s satellite coverage because of a failure in the network.
A failure in the network that causes a message to arrive from a client satellite to a ground station with more that 5 minutes of delay, or not arrive at all.

## Slide 4: Critical failure: Coverage failure
Satellites in range of the client’s satellite: depends of the client’s satellite
Critical failure: failure of all satellites in range of the client’s satellite

## Slide 5: Critical failure: Transmission time failure
Transmission time ≈ 0,5 s
Processing time ≈ 20 s
Time to recognise a link as dead ≈ 45 s
Time to reconfigure the network map ≈ 100 s
Total time ≈ 165 s
Time limit = 300 s
Time to reconfigure 2 successive failures ≈ 310 s
Critical failure: failure of two satellites in the same communication route consecutively

## Slide 6: Critical failure: Ground station failure
If all ground stations fail, the whole constellation fails.
Each ground stations is considered critical
Critical faiure: loss of satellite visibility for any ground station

## Slide 7: Ground segment structure
Mission Control Centre
  Only one
  Located in Terrassa
  Handles all the data
  Checks the constellation status
  Gives instructions to the satellites in case of need
Ground Station
  More than one
  Located across the globe
  Recieves TT&C and HK data and sends it to the Mission Control Centre
  Recieves data from the client satellite and sends it to the client
S-Band
X-Band
Ground Station
MCC

## Slide 8: Ground Station: location
Coverage in different latitudes over time

## Slide 9: Ground Station: location
Coverage in different longitudes over time

## Slide 10: Ground Station: location
Possible optimum Ground Station locations
Final location:
Ground Station 1:
  Canada
Ground Station 2:
  Scotland
Ground Station 3:
  Falkland Islands

## Slide 11: Ground Station: costs
Each Ground Station will consist of:
  100 m2 building
  Communication equipment
  Office equipment
  Electricity
  Water
  Internet connection
  Ground Station license
  Workers

## Slide 12: Ground Station: costs
Two systems: X-band and S-band

## Slide 13: Ground Station: costs
Costs | Canada | Scotland | Falkland Islands
Electricity | 3,500 € | 6,500 € | 6,500 €
Maintenance | 7,500 € | 7,500 € | 7,500 €
License fee | 200 € | 600 € | 600 €
Salaries | 380,000 € | 295,000 € | 125,000 €
Total | 390,000 € | 310,000 € | 140,000 €
Total annual cost of all Ground Stations: 840,000 €

## Slide 14: Mission Control Centre: costs
The Mission Control Centre will consist of:
  500 m2 building
  Office equipment
  Electricity
  Water
  Internet connection
  Workers

## Slide 15: Mission Control Centre: costs
 | Costs
Electricity | 15,000 €
Maintenance | 7,500 €
Salaries | 375,000 €
Total | 400,000 €
Total annual cost of the Mission Control Centre: 400,000 €
Total annual cost of all Ground Stations and the Mission Control Centre: 1,240,000 €

## Slide 16: Summary
Critical failure
  Clear deffinition of a critical failure
Ground segment
  Ground Stations located in Canada, Scotland and Falkland Islands
  Annual cost of all Ground Stations:840,000 €
  Annual cost of the Mission Control Centre: 400,000 €